## Slide 1: OOLAB Custom Orthotics

## Slide 2: Top Cover Materials
Black/Blue ETC
Vinyl Only, 1/16th & 1/8th
Ultrahyde Only, 1/16th & 1/8th
1/8th Black Microcell, Pink/Purple & Blue/Green
1/16th Black Ultrasuede
Diabetic (Poron with Plastazote) (Premium)
1/8th Neoprene
X-Static (Premium)
Brown Sandal Suede (Naot Suede)
Tan Sandal Suede
Perforated 1/16th Leather (Premium)
1/8th Spenco Black (Premium)
*All top covers have Full-length, Sulcus or ¾ length as an option

## Slide 3: Vinyl
  Highly durable vinyl laminated to underlying soft cushion material*
Available in 1/16” and 1/8” thickness as well as Vinyl Only (no poron cushioning)
Key Features:
  Non absorbent
  Highly durable
  Easy to clean
  Minimal Friction
Suitable for: Dress Shoes, Casual Walkers, Casual Shoes
* Vinyl topcovers can be requested to have black nyplex instead of blue poron for cushioning

## Slide 4: Ultrahyde
Soft covering, laminated to 1/16” or 1/8” cushioning* underlay
Also available without cushioned underlay (Ultrahyde Only)
Popular choice of material as it is easy to clean, durable and will not absorb moisture
* Ultrahyde topcovers can be requested to have black nyplex instead of blue poron for cushioning

## Slide 5: 1/8th ETC
Uniform cloth type covering which provides anti-friction and reduces shearing forces while providing moisture wicking capabilities
Key Features:
  Does not absorb moisture
  Tear resistant
  Non-slip
Available in 1/8” thickness -- Blue or Black
Good choice for: Walking, Running & Athletics
*Blue/Black ETC is the DEFAULT top cover if not specified on the Rx – and will be selected based on shoe choice or gender

## Slide 6: Microcell
Closed cell EVA product
Available in 1/8” thickness only
Good option for deep heel cups
Key Features:
  Shock absorbing uniform material
  Easy to clean
  Non-absorbent covering
  Lightweight
Choice of:
  Black
  Green/Blue
  Purple/Pink

## Slide 7: 1/16th Black Suede (Ultrasuede)
1/16" thickness
Suede feel to top surface with black foam, quick recovery foam underlay
Black colour
Suitable for: footwear in which there are limitations in space (i.e.: Dress Shoes)

## Slide 8: Diabetic/Arthtritic (premium)
Available thickness of 1/8” Plastazote + 1/16” Poron
Key Features:
  Shock absorbing uniform material
  Easy to clean
  Non-absorbant
Evenly dissipate shear forces acting on plantar surface of foot (reduces and eliminates friction)

## Slide 9: 1/8th Neoprene
1/8" thickness
Black colour
Key Features:
  Shock absorbing
  Cushioning material surface

## Slide 10: X-Static (PREMIUM)
1/8th in thickness
Made with pure silver, which means there are no chemicals or fear of toxicity to the consumer
Key Features:
  Durable
  Eliminates Odor
  Regulates temperature

## Slide 11: Spenco (Premium)
Only offered as a 1/8th thickness option
Closed cell nitrogen injected material absorbs shock and provides maximum comfort
Ideal for individuals wanting durability combined with heel-to-toe cushioning and comfort
Key Features
  4-way stretch fabric helps reduce friction and heat
  Helps prevent blisters from forming

## Slide 12: Perforated Leather (premium)
Perforated material to allow for moisture control
Ideal for individuals with sweaty feet
Great option for individuals who may be allergic to synthetic materials
Key Features:
  Long lasting
  Thin
  Tear resistant
  Minimal Friction

## Slide 13: 1mm Black Puff
Along with our standard underlay option, 1mm Black Puff may be selected as a top cover
Minimal cushioning
Good option for limitations in space

## Slide 14: Sandal Topcovers
CHOICE OF:
Brown Suede (Naot Suede)
Tan Suede
Black Suede (ultrasuede)
*Choice of top cover WILL be defaulted to selected shoe unless otherwise specified
*Available in 1/16 suede or suede only option per colour

## Slide 15: Underlay Materials
Vinyl
1mm Black Puff
Grey Suede
Durasole
*Additional cushioning may be requested – typically 1mm or extra 1/16th as Nyplex
*Underlay can be full length or forefoot only
*If a heel hole is requested with no underlay, they will receive a circular rubber skid plate

## Slide 16: SHELL MODIFICATIONS

## Slide 17: Heel Cup Height
  Flat
  Shallow
    Typically associated with dress orthotics & footwear
  Standard
    Most common
  Deep
Lab Standards:
< 12mm
12-14mm
16-18mm

## Slide 18: 1st Ray Cutout
Used to increase plantar flexion of the first met shaft
Medial cut out of the orthosis
Indications:
  Sesamoiditis
  Plantarflexed 1st ray
  1st met head pain
  Hallux Valgus (Bunions)

## Slide 19: 1st Met Cutout
<45° cutout of medial/distal end of shell
Indications:
  Hallux Valgus (Bunions)
  1st met head pain

## Slide 20: Heel Hole
Standard 1” and 1.25” hole centrally located in heel cup – filled with poron plug
Indications:
  Heel spurs
  Apply extra relief
  Localized Plantar Fasciitis pain

## Slide 21: Medial/Lateral Flanges (Shell vs Soft)
A medial flange (shell) is an extension of the arch of the shell which projects upward with the apex at the area of the navicular tuberosity
The purpose of the flange is to provide a more direct force at the medial-plantar aspect of the foot in order to offer more control
For some patients, fitting a device with a flange in their shoes can become a problem due to the added bulk of the device in which case a soft flange may be applicable (made out of topcover material)

## Slide 22: Gait Plates
These are for adducted or abducted gait patterns in very young children as well as in adults if necessary
Gait plates limit in-toeing or out-toeing gait caused by rotational deformities of the lower limb
Consist of both medial and lateral flanges and a deep heel cup as well as the gait plate (to induce in-toeing or out-toeing)
Two types:
  In-toe Gait Plate: For out-toeing problems. The medial side extends to the sulcus, tapering to cut out the 4th and 5th mets
  Out-toe Gait Plate: For in-toeing problems. The lateral side extends to the sulcus, tapering to cut out the 1st and 2nd mets

## Slide 23: Orthotic Additions

## Slide 24: Metatarsal Pads & Met Bar
Met. Pad:
Tear shaped modification (poron pad) added to the top of the orthotic
Function:
  Offload pressure from the met. Heads to the metatarsal shafts
Indications:
  Metatarsalgia
  Interdigital Neuroma & Bursitis
Default Placements-
Standard: End of shell
Distal: Moved 6mm distally

## Slide 25: Metatarsal Accom. Pads
Standard 1/8th Nyplex pad extending across the 1st met head to the 5th met head distally to sulcus
Function:
  Provide additional cushioning & redistribution of pressure across the met heads
Indications:
  Decreased fat pad
  Metatarsalgia

## Slide 26: Neuroma Padding
Dome shaped pad placed in the metatarsal interspace between the metatarsal heads
Typically begins at the proximal third of the metatarsal shafts and ends at the met heads
Usually placed between the 2nd-3rd / 3rd-4th interdigital space

## Slide 27: Morton’s Extension
Material (Nyplex, EVA or Rigid) which is added under the first metatarsalphalangeal joint *Rigid requires a polypropylene shell
Function:
  Limit first metatarsalphalangeal R.O.M
Indicated for:
  Dorsiflexed 1st ray
  Hallux Rigidus/Limitus
  Short 1st ray

## Slide 28: Reverse Morton’s Extension
Material (Nyplex or EVA) which is added under the 2nd – 5th metatarsal heads
Indications:
  Plantarflexed 1st ray
  Hallux Valgus (Bunions)

## Slide 29: Heel Cushioning
Standard 1/16th Nyplex cushion pad
Indications:
  Non-centrally located heel spur
  Loss of fat pad
  PF pain
  Rear foot shock absorption

## Slide 30: Heel Spur Padding
Poron “horseshoe” shaped pad applied around heel cup on top of the orthotic
Function:
  Creates a depression
  Lifts calcaneus off the orthotic
Indications:
  Heel spur

## Slide 31: Arch Fill
Padding applied under the arch area of the orthotic plate
Increases rigidity of the orthosis by preventing arch collapse
Applied to the plantar side of the orthotic
Several durometers of fill:
  Soft
  Firm
  Hard

## Slide 32: Arch Cookies (scaphoid pad)
A pad that is plantar and medial to the longitudinal arch and gives extra support and padding to the medial arch area
Several different sizes/thickness:
  i.e.: 1mm, 3mm, 5mm

## Slide 33: Kinetic Wedge/Dancers Pad
‘U’ shaped cutout underneath the first met head
Relieves pressure off of the 1st met head and allows for greater plantarflexion of the 1st met head
Indications:
  Functional Hallux Limitus

## Slide 34: EXTRINSIC POSTINGS

## Slide 35: Neutral
Firm EVA material added to the plantar side of the orthotic
Aids in neutral stabilization of orthotic & calcaneus

## Slide 36: Heel lift
Firm EVA post alongside with additional White EVA
Adds a lift to one orthotic or bilaterally
Maximum height of lift recommended: 10mm (1.0cm)
Indications:
  Leg Length Discrepancy (LLD)
  Achilles Tendonitis

## Slide 37: Varus & Valgus Posting
Rigid orthotics are routinely posted to accommodate the varus or valgus rearfoot and forefoot dispositions
Varus posting helps with a pronated foot or eversion of the calcaneus
Valgus posting helps with a supinated foot or inversion of the calcaneus
Ultimate goal is to maintain a neutral gait cycle by controlling the hind foot

## Slide 38: Medial & Lateral Wedges
Essentially a continuation of a Varus or Valgus post in which extends to the end of the shell
Helps aid/control varying degrees of pronation or supination within the hindfoot, midfoot & forefoot

## Slide 39: Medial & Lateral Forefoot Post
Forefoot pronation or supination can be further controlled with a forefoot post
Forefoot posting is added on the plantar aspect of the shell to position the orthotic in a varus or valgus direction to effectively distribute ground-reactive forces